## Slide 1: ECE480 Team 8: Maximum Power Point Tracker
Daniel Chen
Yue Guo
Luis Kalaff
Jacob Mills
Brenton Sirowatka
Notes: Louis

## Slide 2: Our Team
Name | Responsibility
Daniel Chen | Presentation Preparation
Yue Guo | Lab Coordinator
Luis Kalaff | Project Management
Jacob Mills | Project Webmaster
Brenton Sirowatka | Documentation Preparation
Notes: Louis

## Slide 3: Presentation Objectives
Introduction
Background
Real World Applications
Available Solutions
Project Objectives
Customer Expectations
Design Approach
Design Stages
Implementation
Microcontroller
Voltage and Current Sensing
Testing Strategies
Project Management
Technical Responsibilities
Gantt Chart
Fast Diagram
Notes: Louis

## Slide 4: Background
What is a Maximum Power Point Tracker?
  Maximizes power from solar cells
  The device finds the point on the I-V curve where Maximum Power is given.
  The MPPT matches the low voltage of the solar array to the high voltage of the battery
Notes: Jacob

## Slide 5: Background
There are eight types of methods for tracking the maximum power point:
Perturb and Observe
Incremental Conductance
Current Sweep
Constant Voltage
Open Circuit Voltage
Short Circuit Current
Temperature
Temperature Parametric
We decided to use the Perturb and Observe method.
Notes: Jacob

## Slide 6: Background
Notes: Jacob

## Slide 7: Background
Perturb and Observe Method:
Increases input voltage continuously
Current begins to drop as voltage increases
Once current drops to far the voltage is then lowered back to the point where maximum power is achieved.
The device then oscillates around the maximum power point.
Notes: Jacob

## Slide 8: Real World Applications
MPPTs are used in any product that contains a solar cell.
  Cars, batteries, buses, landscaping, pools, boats, etc.
Also used in optical power transmission systems
  Method for replacing copper wiring with fiber optic cables.
  power is transmitted into light and sent through fiber optic cable.
  Cell converts light back to electricity and sufficient voltage is acquired using MPPT.
Notes: Jacob

## Slide 9: Available Solution
Previously the Solar Car Racing Team used the Dilithium Power Systems ‘Photon Quad MPPT.’
  Boost Ratio: 1 to 14
  contains 160V battery
  Used CAN based communication
Features 4 independent channels and is optimized for several kinds of solar arrays.
Notes: Jacob

## Slide 10: Customer Expectations
Greater than 95% efficiency
One channel
Input voltage 20 to 60 Volts
Output voltage ~110 Volts
Withstand 6 Amps of current
Single PCB
Notes: Brenton

## Slide 11: Design Approach
Notes: Brenton

## Slide 12: FAST Diagram
Notes: Brenton

## Slide 13: Design Stages
DC-DC Boost Converter
Microcontroller Tracking
PCB Layout
Notes: Brenton

## Slide 14: DC-DC Boost Converter
Convert the lower voltage from the solar array to match the higher voltage of the battery
Solar Array
Battery
Notes: Brenton

## Slide 15: PSpice DC-DC Boost Simulation
Notes: Brenton

## Slide 16: Microcontroller Tracking
An algorithm is implemented to find the maximum powerpoint by adjusting the voltage slightly. The team chose to implemented the “perturb and observe” method for maximum power tracking.
Notes: Yue

## Slide 17: Microcontroller
Using C2000 Piccolo launchpad
12bit ADC, 8 PWM channels
60MHz Frequency
Notes: Yue

## Slide 18: Microcontroller
Notes: Yue

## Slide 19: Voltage & Current Sensing
Via Microcontroller
Voltage Divider/Current Resistor Sensing
Notes: Daniel

## Slide 20: Sensing Implementation
Microcontroller
Utilize analog-digital converter
Input constraints
  Need to drop the output voltage from the Solar Array
Notes: Daniel

## Slide 21: Sensing Implementation
Voltage Divider Sensor
Vout
Vout = Vin*(R2/(R1+R2))
Power loss
Non Constant Input
Alternative
Vin
Notes: Daniel

## Slide 22: Sensing Implementation
Current Resistor Sensor
Low ohm Resistor
Less power loss
Notes: Daniel

## Slide 23: PCB Board
Combine the analog and the digital part of our design into one single PCB board
Notes: Daniel

## Slide 24: Testing Strategies
Use a smaller power supply and lower voltages
  eg. Lab Bench Power supply
Limited current for safety
Notes: Daniel

## Slide 25: Technical Responsibilities
Name | Responsibility 1 | Responsibility 2 | Responsibility 3
 | Selection & Ordering | Calculation & Simulations | Prototyping & Refinement
Daniel Chen | Resistor | Risk Analysis Data | Building/Testing Prototype
Yue Guo | Magnetic Core | PCB Layout | Building/Testing Prototype
Luis Kalaff | Microcontroller | Labview DC-DC Booster | Building/Testing Prototype
Jacob Mills | Diode | Inductor Core & Windings | Programming Microcontroller
Brenton Sirowatka | Capacitor | PSpice DC-DC Circuit | Programming Microcontroller
Notes: Louis

## Slide 26: Budget
Design Stages | Cost
DC-DC Boost Converter | $40
Microcontroller | $20
PCB Layout | $60
Miscellaneous | $20
Notes: Louis

## Slide 27: Gantt Chart Tasks
Notes: Louis

## Slide 28: Gantt Chart
Design
Prototype
Refinement
Notes: Louis

## Slide 29: Final Design Blueprint
Notes: Yue

## Slide 30: Special Thanks to
Everyone in the MSU Solar Car Team
  Ian Grosh
  Steve Zajac
  Scott O’Connor
Dr. Bingsen Wang (Faculty Advisor)
Brian,Gregg, and Roxanne (ECE Shop)
Notes: Louis

## Slide 31: Question?
Notes: Everybody

## Slide 32: Thank You
Notes: Everybody