## Slide 1: ECE 480 Design Team 3 Technical Lecture
Arduino Controller Design

## Slide 2: Overview
Arduino Fio and XBee Basics
Joystick Interface
Motor Control
Interrupt Sensor

## Slide 3: Introduction
Based on Microprocessor ATmega328P
  3.3V
  8MHz
C/C++ Based
  http://arduino.cc/en/Reference/HomePage
14 Digital I/O
  6 PWM Available (8bit)
  analog Write() (2 bytes Duty Cycle)

## Slide 4: Introduction Continued
8 Analog Inputs
  10 bit Resolution
  Default Reference (Vcc)
  AREF (0-5V limit)
  analogReference(EXTERNAL)
32KB Flash Memory (Sketches)
  2KB for Bootloader

## Slide 5: Connections
Wired
  Data (pins, header, solder)
  Power (Battery Connector)
  Charging (USB)
Wireless (2.4GHz)
  On-Board XBee Socket
  XBee to USB adaptor (Explorer)

## Slide 6: Wireless Programming
Preparation (for Explorer)
  Short RTS and D3
X-CTU Configuration (Windows)
  Connect
  Run X-CTU
  Set Computer Port (e.g. USB)
  Baudrate (57600, match uC)
  Modem Configuration…

## Slide 7
Parameter | Programming Radio | Fio Radio
ID (PAN Hex) | IDENTICAL | 
BD (Microprocessor) | 6 for (Atmega328) | 6 for (Atmega328)
MY (Source) | (0000 to FFFF) | (0000 to FFFF)
DL (Destination) | FFFF (ALL) My Value (Speecific) | Programmer's MY value
D3 (Digital PIN 3) | 3 (DI) | 5 (DO HIGH)
IC (I/O Change Monitor) | 8 (i.e. 00001000 or D3) | not set
RR (Retries on Send) | 3 | not set
IA (Serial Interrupt) | FFFFFFFFFFFFFFFF (Immune) | 0xFFFF (Modify Allow)

## Slide 8: Digital Joystick Versus Analog Joystick
Joystick types
  Digital Joysticks
  Analog Joysticks

## Slide 9: Interfacing the Analog Joystick to the Arduino Fio
The diagram:
A0 X
A1 Y
The functionality
3.3 v, VCC
GND
10 bit input

## Slide 10
10 bit input /4 = (n*2^10)/(2^2)=(n*2^8)= PWM
  Code:
AnalogRead((10 bit input)/4) ( PWM 0-255, where 255 is 100% duty cycle)
AnalogWrite(pin#,direction) (0<=dir>=255)
AnalogWrite(pin#,PWM) (0<=dir>=255)
Generation of PWM signal

## Slide 11: Power Supply
How to choose a power supply for driving Brushless DC motor
  AC-to-DC Power Supply
  Supply Voltage
  Parallel Connection of Motors
  Rated Supply Current
Mean Well 12V 29A Power Supply

## Slide 12: H-Bridge
How does an H-Bridge work?

## Slide 13
H-Bridge (Cont’d)
How do you pick an H-Bridge motor driver?
  Voltage rating
  Current rating
Pololu 18V 15A Motor Driver

## Slide 14: Brushless DC Motor Feedback
Position
  Rotation count
Speed
  Rotations
  Time
Direction
  Second sensor

## Slide 15: Calculating Position - Simple
Rotations counting
  Photo Interrupter
    “Optical Chopper”
Pulses per rotation
  Gear ratio
Single sensor
  Direction ambiguous
Arduino
  attachInterrupt(pin,ISR,EDGE);

## Slide 16: Position Calculation - Robust
Second Photo Interrupter
  Sensor placement
  Sensor reading
Direction
  Edge Detection
Arduino
  digitalRead(pin);
1
2
1
2

## Slide 17: Speed Calculation
Timing
  Change between pulses
Angular Velocity
  Two sensors
Arduino
  millis() : dTime = millis() – currentTime;
  Rpm = 1/spokeCount * 1/dTime * 1/3600;

## Slide 18
Summary

## Slide 19: Questions?