## Slide 1: MSU Solar Team Battery Management System
Team 7
Matt Gilbert-Eyres, Albert Ware
Gerald Saumier, Auez Ryskhanov
Michael Burch
Facilitator
Dr. Bingsen Wang

## Slide 2: Table of Contents
What Is A Battery Management System
Cell Protection
Communication
Design
Budget
Status/Goals

## Slide 3: What Is A Battery Management System?
Electronically controlled system that manages rechargeable battery cells.
Four Functions
  Cell Protection
  Cell Balancing
  State of Charge
  Communication

## Slide 4: Design Layout
General layout of the system and it features

## Slide 5: Communication Requirements
Communication Board
  8 analog inputs
  4 analog outputs
Display Screen
  Compatible with chosen board
  Possible touch screen for input to system
Sensors
  4 voltage sensors
  1 current sensor
  3 temperature sensors

## Slide 6: Communication Board & LCD Screen
16 Analog Inputs
16 MHz Clock Speed
256 KB Flash Memory
ATmega2560 Microcontroller
3.2” LCD Touch Screen
5V Operation Voltage
Arduino Mega 2560 R3
LCD Touch Screen

## Slide 7: Cell Protection: Sensors
Voltage Sensor (4)
  0.02445-25V input voltage detection range
  0.00489V voltage analog resolution
  Reduces voltage 5x for input to Arduino
Current Sensor (1)
  AC/DC compatible
  Hall Effect
  -50A to 50A current range
Temperature Sensor (3)
  Thermistor Based
  Approx. -40º C to 125º C range

## Slide 8: Cell Protection: Cooling System
2 Fans to cool down the batteries
1 Fan to cool down the Arduino board

## Slide 9: Battery Balancing
Protects the system by balancing the cells to compensate for the differences.
Increase efficiently of system and life of battery
Team currently use passive balancing
Implementation of active balancing

## Slide 10: Passive Balancing
Higher voltage batteries are connected to resistors to lower voltage (balance the cells).
High Losses
Easy to use

## Slide 11: Active Balancing
Move charge from a higher voltage cell to one with the lower charge.

## Slide 12: System Fusing
Fuse type: 10Amp 32 Volt Micro2 Fuse by Littelfuse.
Purpose for fusing the system is to ensure wires and the system are protected in a over current situation.

## Slide 13: System Wiring
Wire size was based on current and voltage requirements.
For our project we will be using 18 gauge wiring (.82mm^2)

## Slide 14: Packaging
Figure2: Battery Box
Figure1: BMS Housing
Figure3: Battery Holder

## Slide 15: Budget

## Slide 16: Motivation
Elithion Lithiumate Pro
  Balancing
  Charge Control
  Price

## Slide 17: Status/Goals
Design aspect is complete
Currently waiting for Parts
Going into the design/prototyping phase
Looking forward to the balancing mechanism

## Slide 18: Thank You
Questions?